COMPUTER NETWORKS
LAB – 4
ROHAN G
CS22B1093
Q1)

Intra Bus Topology Packet Transmission(172.168.1.1 – 172.168.1.3)

Intra Star Topology Packet Transmission (172.168.1.10 – 172.168.1.8)

Intra Star Topology Packet Transmission(172.168.1.11 – 172.168.1.14)

Inter Topology Packet Transmission (172.168.1.5 (Bus Topology) – 172.168.1.15(Mesh Topology))

iii)

Bus Topology -
Performance – Performance reduces as number of users and data transmission at same time increases and has limited bandwidth.

Fault Tolerance – Single break or issue in the network causes the whole network collapse and hence the network stops working.

Star Topology -
Performance – Better in performance compared to Bus topology has it has better bandwidth and can scale to more number of users compared to Bus topology.

Fault Tolerance – Has more fault tolerance if there is a breakage or failure between the switch/hub and the connected network device , but the hub/central switch plays a critical role and failure in it causes the whole network to collapse and stop working.

Mesh Topology -
Performance – Highest performance compared to other two with high bandwidth and low latency due to direct connection between the connected devices in the network.

Fault Tolerance – Has the highest fault tolerance compared two the other two , has a lot of reliability as failure in one of the links , the network still functions . But it is expensive to set it up.

Q2)

I) TCP -

TCP Server -

//CS22B1093 ROHAN G

#include <netinet/in.h>
#include <stdio.h>
#include <stdlib.h>
#include <string.h>
#include <sys/socket.h>
#include <unistd.h>

#define PORT 8080

int main()
{
    int server_fd, new_socket;
    struct sockaddr_in address;

    char buffer[1024] = {0};
    char *hello = "Hello from server";
    socklen_t addrlen = sizeof(address);

    //create a socket file descriptor
    server_fd = socket(AF_INET, SOCK_STREAM, 0);

    if (server_fd == -1) {
        perror("socket failed");
        exit(EXIT_FAILURE);
    }

    //define the server address
    address.sin_family = AF_INET;
    address.sin_addr.s_addr = INADDR_ANY;
    address.sin_port = htons(PORT);

    //bind the socket
    if (bind(server_fd, (struct sockaddr *)&address, sizeof(address)) < 0) {
        perror("bind failed");
        exit(EXIT_FAILURE);
    }

    //listen for connections
    if (listen(server_fd, 3) < 0) {
        perror("listen");
        close(server_fd);
        exit(EXIT_FAILURE);
    }

    printf("TCP Server is running and waiting for messages...\n");

    //accept connection
    new_socket = accept(server_fd, (struct sockaddr *)&address, &addrlen);

    if(new_socket < 0) {
        perror("Connection acceptance failed");
        close(server_fd);
        exit(EXIT_FAILURE);
    }

    //read message from client
    read(new_socket, buffer, 1024);
    printf("Client: %s\n", buffer);

    //send message to client
    send(new_socket, hello, strlen(hello), 0);
    printf("Message sent to client\n");

    //close the socket
    close(new_socket);
    close(server_fd);

}
TCP Client -

//CS22B1093 ROHAN G

#include <arpa/inet.h>
#include <netinet/in.h>
#include <stdio.h>
#include <stdlib.h>
#include <string.h>
#include <sys/socket.h>
#include <unistd.h>

#define PORT 8080

int main()
{
    int sock = 0;
    struct sockaddr_in serv_addr;
    char *message = "Hello from client";
    char buffer[1024] = {0};

    //create a socket file descriptor
    sock = socket(AF_INET, SOCK_STREAM, 0);
    if(sock == -1) {
        perror("Socket creation failed");
        exit(EXIT_FAILURE);
    }

    //define the server address
    serv_addr.sin_family = AF_INET;
    serv_addr.sin_port = htons(PORT);

    //convert IPv4 and IPv6 addresses from text to binary form
    if(inet_pton(AF_INET, "127.0.0.1", &serv_addr.sin_addr) <= 0) {
        perror("Invalid address/Address not supported");
        close(sock);
        exit(EXIT_FAILURE);
    }

    //connect to the server
    if(connect(sock, (struct sockaddr *)&serv_addr, sizeof(serv_addr)) < 0) {
        perror("Connection failed");
        close(sock);
        exit(EXIT_FAILURE);
    }

    //send message to server
    send(sock, message, strlen(message), 0);
    printf("Message sent to server\n");

    //read message from server
    read(sock, buffer, 1024);
    printf("Server: %s\n", buffer);

    //close the socket
    close(sock);
    return 0;
}

Terminal – 1:

Terminal – 2:

II)UDP

UDP Server -

// CS22B1093 ROHAN G

#include <arpa/inet.h>
#include <netinet/in.h>
#include <stdio.h>
#include <stdlib.h>
#include <string.h>
#include <sys/socket.h>
#include <unistd.h>

#define PORT 8080
#define BUFFER_SIZE 1024

int main() {
    int sockfd;
    char buffer[BUFFER_SIZE];
    struct sockaddr_in serv_addr, client_addr;
    socklen_t addr_len;

    // Create socket
    sockfd = socket(AF_INET, SOCK_DGRAM, 0);
    if (sockfd == -1) {
        perror("Socket creation failed");
        exit(EXIT_FAILURE);
    }

    // Define server address
    memset(&serv_addr, 0, sizeof(serv_addr));
    serv_addr.sin_family = AF_INET; // IPv4
    serv_addr.sin_addr.s_addr = INADDR_ANY; // Accept any IP
    serv_addr.sin_port = htons(PORT); // Port

    // Bind the socket to the server address
    if (bind(sockfd, (const struct sockaddr *)&serv_addr, sizeof(serv_addr)) < 0) {
        perror("Bind failed");
        close(sockfd);
        exit(EXIT_FAILURE);
    }

    printf("UDP Server is running and waiting for messages...\n");

    addr_len = sizeof(client_addr);

    // Receive data from the client
    int n = recvfrom(sockfd, buffer, BUFFER_SIZE, 0, (struct sockaddr *)&client_addr, &addr_len);
    if (n < 0) {
        perror("Receive failed");
    } else {
        buffer[n] = '\0'; // Null-terminate the received data
        printf("Client: %s\n", buffer);

        // Respond to the client
        char *response = "Hello from server";
        sendto(sockfd, response, strlen(response), 0, (struct sockaddr *)&client_addr, addr_len);
        printf("Response sent to client\n");
    }

    // Close the socket
    close(sockfd);
    return 0;
}
UDP Client -
// CS22B1093 ROHAN G

#include <arpa/inet.h>
#include <netinet/in.h>
#include <stdio.h>
#include <stdlib.h>
#include <string.h>
#include <sys/socket.h>
#include <unistd.h>

#define PORT 8080
#define BUFFER_SIZE 1024

int main() {
    int sockfd;
    struct sockaddr_in serv_addr;
    char *message = "Hello from client";
    char buffer[BUFFER_SIZE];

    // Create socket
    sockfd = socket(AF_INET, SOCK_DGRAM, 0);
    if (sockfd == -1) {
        perror("Socket creation failed");
        exit(EXIT_FAILURE);
    }

    // Define server address
    memset(&serv_addr, 0, sizeof(serv_addr));
    serv_addr.sin_family = AF_INET;
    serv_addr.sin_port = htons(PORT);
    serv_addr.sin_addr.s_addr = INADDR_ANY;

    // Send message to the server
    sendto(sockfd, message, strlen(message), 0, (const struct sockaddr *)&serv_addr, sizeof(serv_addr));
    printf("Message sent to server\n");

    // Receive response from the server
    socklen_t addr_len = sizeof(serv_addr);
    int n = recvfrom(sockfd, buffer, BUFFER_SIZE, 0, (struct sockaddr *)&serv_addr, &addr_len);
    if (n < 0) {
        perror("Receive failed");
    } else {
        buffer[n] = '\0'; // Null-terminate the received string
        printf("Server: %s\n", buffer);
    }

    // Close the socket
    close(sockfd);
    return 0;
}
Terminal -1 :

Terminal – 2 :

Q3)
UDP Server -
//CS22B1093 ROHAN G

#include <stdio.h>
#include <stdlib.h>
#include <string.h>
#include <unistd.h>
#include <arpa/inet.h>
#include <sys/types.h>
#include <sys/socket.h>

#define MAXLINE 1024

int main() {
    int sockfd;
    char buffer[MAXLINE];
    const char *hello = "Hello from Rohan";
    struct sockaddr_in servaddr, cliaddr;
    socklen_t len;

    // Create socket
    if ((sockfd = socket(AF_INET, SOCK_DGRAM, 0)) < 0) {
        perror("socket creation failed");
        exit(EXIT_FAILURE);
    }

    memset(&servaddr, 0, sizeof(servaddr));
    memset(&cliaddr, 0, sizeof(cliaddr));

    servaddr.sin_family = AF_INET;
    servaddr.sin_addr.s_addr = INADDR_ANY;
    servaddr.sin_port = htons(8080);

    if (bind(sockfd, (const struct sockaddr *)&servaddr, sizeof(servaddr)) < 0) {
        perror("bind failed");
        close(sockfd);
        exit(EXIT_FAILURE);
    }

    len = sizeof(cliaddr);

    int n = recvfrom(sockfd, (char *)buffer, MAXLINE, MSG_WAITALL, (struct sockaddr *)&cliaddr, &len);
    buffer[n] = '\0';
    printf("Client : %s\n", buffer);

    sendto(sockfd, (const char *)hello, strlen(hello), 0, (const struct sockaddr *)&cliaddr, len);

    close(sockfd);
    return 0;
}
UDP Client -
//CS22B1093 ROHAN G

#include <stdio.h>
#include <stdlib.h>
#include <string.h>
#include <unistd.h>
#include <arpa/inet.h>
#include <sys/types.h>
#include <sys/socket.h>

#define MAX 1024

int main() {
    int sockfd;
    char buffer[MAX];
    const char *message = "Hello from ROHAN";
    struct sockaddr_in serv_addr;
    socklen_t len;

    if ((sockfd = socket(AF_INET, SOCK_DGRAM, 0)) < 0) {
        perror("socket creation failed");
        exit(EXIT_FAILURE);
    }

    memset(&serv_addr, 0, sizeof(serv_addr));

    serv_addr.sin_family = AF_INET;
    serv_addr.sin_port = htons(8080);

    if (inet_pton(AF_INET, "172.16.25.82", &serv_addr.sin_addr) <= 0) {
        perror("Invalid address or Address not supported");
        close(sockfd);
        exit(EXIT_FAILURE);
    }

    sendto(sockfd, (const char *)message, strlen(message), 0, (const struct sockaddr *)&serv_addr, sizeof(serv_addr));

    len = sizeof(serv_addr);
    int n = recvfrom(sockfd, (char *)buffer, MAX, MSG_WAITALL, (struct sockaddr *)&serv_addr, &len);
    buffer[n] = '\0';
    printf("Server : %s\n", buffer);

    close(sockfd);
    return 0;
}

UDP Server (me) , friend is Client -

UDP Client (me) , friend is Server -